## Slide 1: New Horizons SPICE Review NH-J/P/SS-SPICE-6-V1.0
Tony Farnham

## Slide 2: SPICE Data
Data set NH-J/P/SS-SPICE-6-V1.0
Accumulating data set
Kernel set created by the SOC for use in scientific data analysis
  Not always compatible with the kernels used for Mission Ops.
Current release includes latest instrument alignment data
  Differ from image data values?

## Slide 3: Documentation
Catalog files
  Typically well done, no major issues
    Much info taken from other sources
  Some typos (separate file)
  PERSON.CAT file has A’Hearn as first contact
    Correct/intentional/desired?
Labels
  No significant issues
  TARGET_NAME in all cases is “Jupiter, Pluto, Solar System”. Should this be more focused?

## Slide 4: Documentation
Data files
  Extensively documented, as usual
  Tried to check to make sure text agrees with kernels
    Assuming values are correct
  Comments in some files are not correct/relevant
    Came from individual files merged into one
    Not particularly important (e.g. how to invoke CKBRIEF)
  Some typos (separate file)

## Slide 5: Reading Data
Read all kernels with no problems
  Used FURNSH list provided in the metadata
  Some kernels differ from those used in NH datasets
    Assume that this dataset is most up-to-date or that the archive uses merged files

## Slide 6: Testing the Data
Adapted my general geometry routine for NH data
Randomly sampled data at various times throughout the dataset to test temporal calculations
  Seem to be valid for times when the s/c was not in hibernation
Calculations for s/c and planets
  State vectors, rates, etc.
  Seems robust and complete
Tried to test some aspects of all data, instruments, etc. at some level
  Not familiar with some instruments so not sure how to fully exercise them

## Slide 7: Instruments
Able to read instrument files, grab instrument FOV properties and compute various dependencies
  Boresight pointing, corner positions, etc
  Exception is Ralph, addressed in errata file
Instruments are body-mounted to the s/c, so they should be simple coordinate transformations relative to the spacecraft frame
  Compared boresight pointing for various instruments, and it seems consistent
  Assume if some instruments are correct, all will be
  Test some instruments extensively (LORRI, REX)

## Slide 8: Testing Against Data
Used LORRI and REX data sets as comparative test
  My values generally match header and label values in a random sampling of those files
  LORRI boresight often differed by a few tenths of a degree
    Old alignment information in image data files?
More extensive tests with LORRI data
  How would I use the data?
  Looked at pointing throughout Jupiter encounter in Feb 2007

## Slide 9: Jupiter Encounter Pointing
Jupiter and Io
  Position of boresight, relative to Jupiter
    Triangles – Jupiter images
    Diamonds – Io images
    Tracks are computed position of Io
LORRI seems to be self consistent

## Slide 10: Jupiter Encounter Pointing
Jupiter and Europa
  Position of boresight, relative to Jupiter
    Triangles – Jupiter images
    Diamonds – Europa images
    Tracks are computed position of Europa
LORRI seems to be self consistent

## Slide 11: Summary
Files are readable and well-documented
  Few typos
LORRI calculations seem to be self-consistent and correct
REX calculations seem to be self-consistent
Other instruments are consistent with LORRI and REX
  By extension, they should be correct as well
Temporal coverage seems to be complete
Data set is in good shape