## Slide 1: Venetia Burney Student Dust Counter (SDC)
EPO activity put together and maintained by students (U. Colorado)
Impact dust detector
  Map the special and size distribution of dust along New Horizon’s path
PVDF film detectors
  Permanently polarized film
  Impact cause spontaneous depolarization
  Depolarization charge depends on particle momentum
  Charge Mass (assuming vparticle = vNH)
  Detectable Mass Range of 10-12 to > 10-9 grams
Thruster firings, etc., also depolarize
  Most data taken during cruise
  Interested in dust population along entire route
  Fewer false positives

## Slide 2: Supporting Document Issues
Sdc_ssr – “The Student Dust Counter on the New Horizons Mission”, Horanyi, et al. (2007) preprint
Can we get the final copy of this paper INSTEAD OF THE PREPRINT?
Soc_inst_icd – New Horizons SOC to Instrument Pipeline ICD (July 2014)
On page 118 under Section 13.1.1 it says that Channel 11 failed before launch. On Page 119 under Section 13.2.1 it says that Channel 10 has an electrical issue. Other documentation makes it clear it is Channel 11 that has the issue.
I think that having the data number large for a small event and small for a large event is possibly confusing, though not fatally so.
The first paragraph in section 13.3.1.1 repeats the previous paragraph.
The last paragraph in section 13.3.1.1. cites a 2007 paper as being “in pub”. We should have the updated citation here.
Section 13.4.2 shows the Dataflow Block Diagram. The lower green rectangle should say “Conversion of Charge to Mass” instead of repeating the upper green rectangle.

## Slide 3: More Supporting Document Issues
Soc_inst_icd_acroabbr – list of acronyms and abbreviations
Within the database acronyms should have a unique meaning to minimize confusion. In these cases we should pick a single acronym for a single phrase and do a find/replace to get rid of the rest.
“ApID” and “APID”
“G&C”, “GN&C”, and “GNC”
“MOPs” and “MOPS”
Bigger problem for SOC and SOCC – let’s not use the same acronym for both “Science Operations
Center” and “Solar Occultation Channel”.
In the various documents we see SDC, VSDC, and VB-SDC all to refer to the same instrument –
pick one. I prefer SDC, which is used most of the time (including the literature paper), none of the variants occur on the acronym list.
Soc_inst_icd_sdc – overview of the SDC instrument
Contains formatting for data files
If Channel 11 failed but still generate spurious data which is processed, is there any reason to archive
these data?

## Slide 4: Data Issues
None detected
DN appears to be processing DN to charge and mass of particles as per spec
Archival Quality
But not clear that the instrument is collecting significant data (Science Team is aware)
Mass, threshold, std dev all same order of magnitude (10-12 g)
only a few percent in 10-11 g range (largest I found 16×10-12 g )
If rocky, then all found to be in 1 – 2 µm range
typical size near Earth is 10 – 100 µm
Pioneer 10, 11 found density of particles > 10 µm constant out to 18 AU
beta meteoroids typically 10-12 grams (as seen here)
Control, and active detectors returning similar values
Preflight predictions about 1 dust particle/week (400 by now)
Launch on 12/10/2006 collected 53 in 1.7 hr (126,000 dust particles/week)
Launch on 12/22/2006 collected 12 in 36 hr (75/week)
Jupiter on 6/9/2007 collected 30 in 51 hr (100/week)
Jupiter on 6/24/2007 collected 30 in 48 hr (69/week)
Pluto on 12/20/2010 collected 30 in 32 hr (156/week)
Pluto on 6/16/2014 collected 2 in 2 hr (177/week)