## Slide 1: Rosetta PDS Review
ROSINA, COSAC & PTOLEMY
Reviewer: Heather Franz
2/15/16 – 2/17/16

## Slide 2: ROSINA

## Slide 3: ROSINA Overview
ROSINA = Rosetta Orbiter Spectrometer for Ion and Neutral Analysis
  Two mass spectrometers for neutrals and primary ions
  Complementary capabilities as pressure sensor
Two types of data
  Mass spectra
  Pressure records

## Slide 4: ROSINA science objectives
ROSINA primary objectives
  To determine elemental, isotopic and molecular composition of the comet atmosphere and ionosphere
  To measure temperature and bulk velocity of gas
  To determine homogeneous and inhomogeneous reactions of gas and ions in dusty atmosphere and ionosphere

## Slide 5: ROSINA sensors (1)
DFMS (double focusing mass spectrometer)
  High resolution mass spectrometer with magnetic sector analyzer
  Two basic operating modes - Gas mode & ion mode
  Three detectors – multichannel plate (MCP), channel electron multiplier (CEM), Faraday cup (FC)
  In-flight calibration – small gas tube introduces calibrated amounts of noble gas mixture into source

## Slide 6: ROSINA sensors (2)
RTOF (Reflectron Time-of-Flight) mass spectrometer
  Two almost independent mass spectrometers
    Storage channel – for cometary neutral particles
    Ortho channel – orthogonal extraction source for cometary ions
  Micro-channel plates (MCPs) of imaging quality for detector
  Gas Calibration Unit (GCU) – injects defined quantity of known gas mixture (He, CO2 & Kr) into either the storage source or orthogonal source

## Slide 7: ROSINA sensors (3)
COPS
  Two sensors
    Nude gauge – measures total pressure (total neutral particle density) of cometary gas
    Ram gauge – measures ram pressure, equivalent to cometary gas flux
  Generated ion currents are measured by high-sensitivity electrometers

## Slide 8: ROSINA RIDs
See Excel spreadsheet

## Slide 9: ptolemy

## Slide 10: Ptolemy overview
Ptolemy is a miniature gas-processing laboratory
  Uses chemical processing, GC, in situ calibration and mass spectrometry
  Determines nature, abundance and stable isotope compositions of volatile species
Primary science goal – isotope ratios
  To determine 13C/12C, 15N/14N, 18O/16O, 17O/16O and D/H ratios of major constituents of a comet.

## Slide 11: Ptolemy subsystems
Sample Collection (SC)
  Primarily Sample Drilling and Distribution unit (SD2)
  Lander oven/carousel for solid samples (ice/organics/silicates) extracted from nucleus by drilling
  Coma samples are cryogenically trapped on adsorbent in a high-T oven (CASE oven), then heated to release volatiles
Gas Distribution and Processing System (GDPS)
  Heaters, valves, T & P sensors
  Ovens can heat to 800C (high-T ovens) or 180C (med-T ovens)
  Med-T ovens are shared by Ptolemy, COSAC and CIVA-ROLIS
Gas Chromatography (GC)
  3 GC columns with He carrier gas
Mass Spectrometer (MS)
  Ion trap MS with mass range of 15-150 amu and mass resolution better than unity

## Slide 12: Ptolemy measurements
GC measures retention times of molecular species in separation columns
MS measures m/z ratio of ionized fragments of molecular species
T and P of various components are monitored

## Slide 13: Ptolemy RIDs
See spreadsheet

## Slide 14: cosac

## Slide 15: COSAC overview
COSAC = Cometary Sampling and Composition experiment
Science objective
  Identify volatile molecular species in cometary nucleus, especially high-MW organic compounds and chiral analysis
  Observe variations in volatile compounds evolved from nucleus as function of solar distance

## Slide 16: COSAC instruments
Gas chromatograph (GC)
  GC with 8 columns and TCDs –
  Measures retention times of molecular species
Time-of-flight mass spectrometer (TOF)
  Multi-sphere plate secondary electron multiplier detector
  Measures time-of-flight of ionized fragments of molecular species
  Can achieve higher resolution by reflectors for multi-turn mode

## Slide 17: COSAC measurements
Atmosphere or solid samples
  Sample collection (SD2 unit) shared with Ptolemy
Pyrolysis ovens
  Med-T ovens – heat to 180C, shared with Ptolemy
  High-T ovens – heat to 600C
  Stepwise heating for 64 levels between -100C and +600C
Calibration
  Includes onboard calibration gas with He, Ne, Kr, and Ar
  Used to fine-tune voltages, calibrate TOF-MS and check GC performance

## Slide 18: COSAC RIDs
See spreadsheet