## Slide 1: Rosetta Lander MAG Data Review Comment Summary rl-cal-romap-2-pdcs-mag-v1.0 rl-cal-romap-2-phc-mag-v1.0 rl-c-romap-2-fss-mag-v1.0 rl-c-romap-2-rbd-mag-v1.0 rl-c-romap-2-sdl-mag-v1.0 rl-cal-romap-3-pdcs-mag-v1.0 rl-cal-romap-3-phc-mag-v1.0 rl-c-romap-3-fss-mag-v1.0 rl-c-romap-3-rbd-mag-v1.0 rl-c-romap-3-sdl-mag-v1.0 rl-cal-romap-5-pdcs-mag-v1.0 rl-c-romap-5-fss-mag-v1.0
S. Joy

## Slide 2: Summary – Lander Raw (-2-) MAG data sets
All of the files in each data set are properly described by their labels allowing the user to read and interpret the bytes in the data files
The documentation is very sparse.
  There is no detailed timeline explaining activities on the spacecraft that might help the user understand the sharp jumps in the field or in the reference voltages
  There is no explanation of how the changes in the reference voltages (both nearly instantaneous and slow drifts) might impact the calibration
The data are “usable” in there current state but it would be difficult for another team to develop an independent calibration of the magnetometer without additional documentation.
Data can be “certified” as is, however, these data sets would be significantly improved by additional documentation.
RIDs
  Fix typos/misspelled words in various files

## Slide 3: Summary – Lander Calibrated (-3-) MAG data sets
In general, the preliminary calibrations that have been applied to these data do not remove all of the instrumental/spacecraft contamination
  The field magnitude is commonly off by orders of magnitude
  There are numerous quasi-periodic noise sources with periods between 10-30 seconds
  While it is understood that the calibration is preliminary, the data set catalog descriptions could/should(?) be updated to describe the noise sources and if any further attempt will be made to remove them
RIDs
      RL-C-ROMAP-3-FSS-MAG-V1.0 - Error in dataset.cat terse description: "This data set contains raw data referred to FSS Mission Phase“
      RL-C-ROMAP-3-FSS-MAG-V1.0 - Error in the record_length (165 -> 168) in all data labels
      Fix typos/misspelled words in various files

## Slide 4: Summary – Lander Calibrated (-5-) MAG data sets
In general, the final calibrations that have been applied to these data remove most of the instrumental/spacecraft contamination
  The field magnitude is plausible (<10 nT)
  There are numerous quasi-periodic noise sources in the pre-delivery data set
  Level-5 data are provided for only a small subset of the total time period. Since these are the only data that are readily usable for science, it would be good to have a complete data set.
These data are generally in good shape!
RIDs
  No data set specific RIDs