## Slide 1: Rosetta Orbiter RPCICA Archive Comments ro-c-rpcica-2-esc1-raw-v1.0 ro-c-rpcica-2-prl-raw-v1.0 ro-c-rpcica-3-esc1-calib-v1.0
S. Joy

## Slide 2: Overview
All of the ro-c-rpcica* review volumes share a large number of common files: catalog files, documents, required files (Xxinfo.TXT), etc. rather than repeating comments on those files in every presentation my comments are all included here
Most of the common files have been previously reviewed so there is an expectation that the files would be in pretty good shape.

## Slide 3: Root Directory Files
ro-c-rpcica-2-esc1-raw-v1.0
  aareadme.txt and voldesc.cat present and acceptable
ro-c-rpcica-2-prl-raw-v1.0
  aareadme.txt and voldesc.cat present and acceptable
ro-c-rpcica-3-esc1-calib-v1.0
    aareadme.txt and voldesc.cat present and acceptable

## Slide 4: Catalog Files
catinfo.txt (refers to “person.cat”, directories contain “pers.cat”)
mission.cat (various typos, content fine)
insthost.cat (various typos, content fine)
reference.cat
inst.cat (various typos, content fine)
software.cat
person.cat
dataset.cat - ro-c-rpcica-2-esc1-raw-v1.0 – sparse,
  RID: file describes binning of the data in mass but this does not appear to be the case, at least not in all of the L2 files. Description should state that these are raw data in data numbers and explain why so many of the values are either zero or single digit numbers.
dataset.cat - ro-c-rpcica-2-prl-raw-v1.0 – sparse.
    RID: file describes binning of the data in mass but this does not appear to be the case, at least not in all of the L2 files. Description should state that these are raw data in data numbers Description should state that these are raw data in data numbers and explain why so many of the values are either zero or single digit numbers.
dataset.cat - ro-c-rpcica-3-esc1-raw-v1.0 – sparse,
  RID: description should state that these are calibrated data in units of “flux” and explain why so many of the values are zero.

## Slide 5: Document
docinfo.txt (all volumes)
ica_eacid Subdirectory
  ica_eaicd.pdf (.lbl, .asc, .doc) ok
  ica_l2_to_l3_eacid (.lbl)
    RID: Document should provide a concrete example starting with a specific data file, walking through the lookup of the appropriate calibration tables and values
Software Subdirectory
  Various MATLAB programs to initialize, read, and plot the ICA data described by the PDS labels as ASCII documents
  Softinfo.txt – RID: Please add a statement providing the version of MATLAB used to produce the code, another indicating that the software is unsupported, and lastly, add a brief statement of how to use the programs provided.
ica_cal.pdf (lbl) – ok, no changes requested
ica_cmd_brief.pdf (lbl) – ok, no changes requested
icatables.pdf (lbl) – ok, no changes requested
icma_tctm.pdf (lbl) – ok, no changes requested

## Slide 6: Calib Directory
calinfo.txt – meets the minimum requirement
    Not very useful description of the 25-140 calibration tables and their usage. Should point the user to the ica_l1_to_l3_eacid.pdf file on the level 3 volumes
  ica_el_table_v0*.tab (.lbl) ok
  ica_energy_table_v0*.tab (.lbl)
  ica_mass_look_up_table*_v0*.tab (.lbl)
  gfactor_heavy_v0*.tab (.lbl)
  gfactor_light_v0*.tab (.lbl)
  ica_mask_heavy_bst_p*_v0*.tab (.lbl)
  ica_mask_heavy_nm_p*_v0*.tab (.lbl)
  ica_mask_light_bst_p*_v0*.tab (.lbl)
  ica_mask_light_nm_p*_v0*.tab (.lbl)
  ica_mass_look_up_table*_v0*.tab (lbl)

## Slide 7: Geometry Files
geominfo.txt – meets minimum requirement
  Add statement that says that these figures are extracted from the EACID
ica_fov.jpg (.lbl)
ica_location.jpg (.lbl)
sectors.pdf (.lbl)

## Slide 8: Index Files
indxinfo.txt
  Does not mention checksum file or its usage, consider adding
index.tab (.lbl)
browse_index.tab (.lbl)
checksum.tab (.lbl)

## Slide 9: Data: ro-c-rpcica-2-XXXX-raw-v1.0
For each hour that contains data, there are 3 data files plus labels for each
  Data - rpcica141130t00_000_96l2.tab (.lbl) - 10-75 MB each
    Values are likely to be correct, difficult to compare to browse plots provided
    2048 records per time step (16x4x16 azimuth x elevation x mass)
    RID: Data appear to be binned in elevation angle. If this was done on the ground, then this is not L2 data. This appears to be a mistake in this particular file. Other files that were spot checked did not appear to have binning in elevation angle.
  HSK - rpcica141130t00_000_hk.tab (.lbl)
  Geom - rpcica141130t00_000_geom.tab (.lbl)
    Spacecraft position, velocity, altitude, etc.
    RID: Geometry information in the labels and data files have too many significant digits
    RID: Provide SPICE kernel set used to produce files in label
All files are simple ASCII tables
  Nearly every record contains value of 00000 for the counts in all 96 channels.
  RID: Data are nearly all zero with occasional single digit numbers. This should be described and explained in the dataset.cat. Browse plots seem to show more data content and variability.
Data are difficult to work with because of their size in this format but no changes are proposed at this time
Browse plots suggest that there may be some issues in the separation of the solar wind (light) and water group (heavy) particles.

## Slide 10: Data: ro-c-rpcica-3-esc1-raw-v1.0
For each hour that contains data, there is a data file and label
  Data - rpcica141128t05_000_96l3.tab (.lbl) - 60-75 MB each
    512 records per time step 16x16x2 (azimuth x elevation x mass)
      L2 data were different 16x4x16 (azimuth x elevation x mass)
    Values are likely to be correct, difficult to compare to raw data for same time period
    Browse plots would be nice (plots on raw volumes might be more appropriate here
    RID: Geometry information in the labels have too many significant digits
    RID: Data are binned in mass
All files are simple ASCII tables
  Nearly every record contains value of 0.000E+00 for the counts in all 96 channels.
  RID: Explain the abundance of zero values in the data files and why it is so difficult to correlate the data files with the browse plots
Data are difficult to work with because of their size in this format but no changes are proposed at this time

## Slide 11: Browse: ro-c-rpcica-2-XXXX-raw-v1.0
Browinfo.txt – present, not useful.
  Plots appear to be calibrated data, not the raw data that are on the volume making it difficult to compare the two
  RID: Please include a description of how the plots were generated from the data files (sum over azimuth and elevation angles and convert energy step to eV?)
Plots include full day and each hour of the day that contain data
Full day
Hour 0 - 1

## Slide 12: Summary
The data contain a very large number of zeros with only a small number of single digit numbers. This is inconsistent with my expectations given the richness of the browse plots.
RIDs:
  All: data set catalog file descriptions should be updated to include discussion of precessing level, units, and the sparseness of the data.
  All: Provide information in the calinfo.txt that describes the differences between files of similar name rather than just a list of file names (add naming conventions for each file type).
  L2 volumes: browinfo.txt should include description of how the plots were created (angular binning?, apply calibration?, etc.)
  ro-c-rpcica-3-esc1-calib-v1.0: Provide concrete example of how to produce an L3 file from one of the files on the L2 volume including which calibration table to apply based on the contents of the L2 data values in the ica_l2_to_l3_eacid document.
  ro-c-rpcica-2-esc1-calib-v1.0: file rpcica141130t00_000_96l2.tab appears to be incompatible with the rest of the data set (binned in elevation angle).
  ro-c-rpcica-2-XXXX-calib-v1.0: Update labels of the *geom.tab to specify the set of kernels used to produce the geometry data i.e.SPICE_FILE_NAME = {“file1”, “file2”, … “fileN”}
  ro-c-rpcica-2-XXXX-calib-v1.0: Update the *geom.tab files to have an appropriate number of significant digits in the data columns.