## Slide 1: Rosetta Lander ROMAP Common File Comments
S. Joy

## Slide 2: Overview
All of the rl-*romap* review volumes share a large number of common files: catalog files, documents, required files (Xxinfo.TXT), etc. rather than repeating comments on those files in every presentation my comments are all included here
Most of the common files have been previously reviewed so there is an expectation that the files would be in pretty good shape.

## Slide 3: Catalog Files
catinfo.txt
mission.cat (various typos, content fine)
insthost.cat (various typos, content fine)
inst.cat (various typos, content fine)
software.cat
ref.cat
person.cat

## Slide 4: Documents other than the calibration description
docinfo.txt
eaicd_romap.pdf (.lbl)
rl_romap_logbook.txt (.lbl)
ro-lro-dp-300002-ua.pdf (.lbl)
romap_calibration_desc.lbl
timeline_phc.png (.lbl)
timeline_phc.txt
timeline_phc_desc.txt

## Slide 5: romap_calibration_desc.txt
This document is acceptable but could be improved significantly
  There is no description of any effort to correlate the timing between instrument components (mag, spm). Each component has internal timing delays associated with digitization, internal filters, readout times, electronic processing, etc. None of these effect are described or characterized.
  It does not appear as though any ground calibration of the magnetometer sensor has been included, in particular, work to determine the orthonalization matrix the 3 sensors (impossible to assemble 3 sensors in a perfectly orthogonal configuration). Impact to science of not orthogonalizing on a non-spinning spacecraft is small.
  There appears to be no effort to confirm that the final deployment geometry matched the expected state (rotation matrix is pure 1’s and 0’s).

## Slide 6: INDEX files
indxinfo.txt - Add a discussion of the checksum files and their usage (MD5 tools), in particular, that they reference files from the root of the volume and not relative to the INDEX directory where the files are located.
index.lbl
index.tab
checksum.lbl
checksum.tab

## Slide 7: LABEL
labinfo.txt
Format files discussed with the labels of the various products that they describe

## Slide 8: Summary
Other than fixing a few misspelled words, the common files are in good shape.
  romap_calibration_desc.txt could/should be improved