## Slide 1: NH REX Pluto Encounter PDS/SBN Data Review
Dick Simpson
19 May 2016
University of Maryland
College Park, MD

## Slide 2: REX Science Objectives
Pluto:
Atmospheric/Ionospheric Structure
Radius from length (time) occultation chord
Day and night side surface temperature from radiometry
Mass from trajectory deflection*
Charon:
Same as for Pluto (to the extent possible)
Late Addition:
Pluto surface electrical properties from BSR#
* Not included in these data sets
# Bistatic radar — oblique reflection from Pluto’s surface

## Slide 3: Observation Geometry
Pre-encounter tracking for gravity
Signal refraction for atmosphere and ionosphere
Dark side radiometry and chord
Post-encounter tracking for gravity
Repeat for Charon
v
Exit occultation
Adapted from https://blogs.nasa.gov/pluto/2015/11/13/radio-signals-from-earth-probe-plutos-atmosphere/ by W. Woods

## Slide 4: Spacecraft Instrumentation
40
5
GRAVITY
RADIOMETRY
OCCULTATION
RAW ARCHIVAL DATA:
5 byte radiometry samples
2x2 byte I/Q voltage samples
3 byte time tags
CALIBRATED ARCHIVAL DATA:
Same as above as 4-byte floats
Adapted from Tyler et al., SSR, 2008

## Slide 5: REX Output Frame (ROF)
FPAG samples from one time unit (1.024 s)
  1250 pairs of 2-byte I, 2-byte Q voltage samples — 5000 B
  10 5-byte accumulations* of radiometry ‘power’ — 50 B
  10 3-byte time tags** — 30 B
  ROF ID byte — 1 B
  Input select status byte (science + 7 tests) — 1 B
  Spares — 6 B Total — 5058 B
Stored in one FITS file with 2880 byte records
* Reset to 0 every 1.024 s
** Reset to 0 at every REX initialization

## Slide 6: ROF Stucture (raw data starting in FITS record 7)
ID | I[1] MSB | I[1] LSB | STATUS | Q[1] MSB | Q[1] LSB
R[1] MSB | I[2] MSB | I[2] LSB | R[1] 4SB | Q[2] MSB | Q[2] LSB
R[1] 3SB | I[3] MSB | I[3] LSB | R[1] 2SB | Q[3] MSB | Q[3] LSB
R[1] LSB | I[4] MSB | I[4] LSB | T[1] MSB | Q[4] MSB | Q[4] LSB
T[1] 2SB | I[5] MSB | I[5] LSB | T[1] LSB | Q[4] MSB | Q[4] LSB
I[6] MSB | I[6] LSB | Q[6] MSB | Q[6] LSB | I[7] MSB | I[7] LSB
Q[7] MSB | Q[7] LSB | I[8] MSB | I[8] LSB | Q[8] MSB | …
I/Q pairs continue through Q[125] LSB.
The structure repeats with R[2], T[2], and more I/Q pairs.
The ROF ends in the middle of FITS record 8 with Q[1250] LSB.
The remainder of record 8 is undefined.

## Slide 7: FITS File Organization (raw data)
PDS_VERSION_ID = PDS3
RECORD_TYPE = FIXED_LENGTH
RECORD_BYTES = 2880
FILE_RECORDS = 26
^HEADER = “FILE”
^ARRAY = (“FILE”, 7) ROF is here (2 recs)
^EXTENSION_IQVALS_HEADER = (“FILE”, 9)
^EXTENSION_IQVALS_TABLE = (“FILE”, 10) unpacked I/Q samples
^EXTENSION_RAD_TIME_TAGS_HEADER = (“FILE”, 12)
^EXTENSION_RAD_TIME_TAGS_TABLE = (“FILE”, 13) unpacked time tags
and radiometer values
…

## Slide 8: EXTENSION_RAD_TIME_TAGS_TABLE (unpacked raw data in FITS record 13) Radiometry and time tag values are unpacked and stored as pairs of 8-byte and 4-byte (respectively) unsigned integers in time order (120 B total)
EXTENSION_IQVALS_TABLE (unpacked raw data, starting in FITS record 10)
I and Q pairs are unpacked and stored as pairs of 2-byte MSB signed integers in time order (5000 B total)

## Slide 9: FITS File Organization (calibrated data)
PDS_VERSION_ID = PDS3
RECORD_TYPE = FIXED_LENGTH
RECORD_BYTES = 2880
FILE_RECORDS = 26
^HEADER = “FILE”
^IMAGE = (“FILE”, 7) ROF repeats here
^EXTENSION_IQVALS_HEADER = (“FILE”, 9)
^EXTENSION_IQVALS_TABLE = (“FILE”, 10) I/Q samples REAL*4
^EXTENSION_RAD_TIME_TAGS_HEADER = (“FILE”, 14)
^EXTENSION_RAD_TIME_TAGS_TABLE = (“FILE”, 15) unpacked time tags
and radiometer REAL*4
…

## Slide 10: EXTENSION_RAD_TIME_TAGS_TABLE (calibrated data in FITS record 15) Radiometry and time tag values are unpacked and stored as pairs of 4-byte MSB REAL*4 numbers in time order (80 B total). Calibration scales radiometer to power in dBm and time tags to seconds since REX initialization.
EXTENSION_IQVALS_TABLE (calibrated data, starting in FITS record 10)
I and Q samples are unpacked and stored as pairs of 4-byte MSB REAL*4 numbers in time order (10 kB total).
Calibration scales sample values to ±1000 mv at input to ADC.

## Slide 11
Chart: NH REX Raw Radiometry from 20150714_029918 0x7b1
REX INITIALIZATION
OVERVIEW OF RAW DATA
ACTIVITY IDENTIFICATION IS EDUCATED GUESS

## Slide 12
Chart: NH REX Raw Radiometry from 20150714_029918 0x7b1
REX INITIALIZATION: TWO RECORDS WITH ALL ZEROES
DAY SIDE EMISSION
NIGHT SIDE EMISSION

## Slide 13
Chart: NH REX Raw Radiometry from 20150714_ 029918 0x7b1
REX INITIALIZATION: TWO RECORDS WITH ALL ZEROES
DAY SIDE EMISSION?

## Slide 14
Chart: NH REX Raw Radiometry from 20150714_029918 0x7b1
NH HGA TO EARTH POINT WITH DSN TRANSMITTER ON
COLD SKY PLUS DSN SIGNAL

## Slide 15
Chart: NH REX Raw Radiometry from 20150714_029918 0x7b1
OCCULTATION FOLLOWED BY NIGHTSIDE SCAN
OCCULTATION
COLD SKY PLUS DSN SIGNAL
DIFFRACTION OVERSHOOT

## Slide 16
Chart: NH REX Raw (I,Q) Values from 20150714_029918 ENG_0x7b1
Geometric occultation —
Decay to 50% at ~45915.4

## Slide 17
Chart: NH REX Average Squared (I,Q) from 20150714_029918
DIFFRACTION PATTERN
FREE SPACE POWER LEVEL
GEOMETRIC OCCULTATION
-----------------------------------
BEGINNING OF CHORD

## Slide 18
Chart: NH REX Calibrated (I,Q) Averaged over 0.01 s from 20150714_029918 SCI_0x7b1
ZOOM TO INGRESS OCCULTATION FROM CALIBRATED DATA

## Slide 19
Chart: NH REX Calibrated Radiometer Output from 20150519_029434 SCI_0x7b1

## Slide 20
Chart: NH REX Calibrated Radiometer Output from 20150519_209434 SCI_0x7b1

## Slide 21
Chart: NH REX First ROF (I,Q) from 20150519_029434 rex_0294345061_0x7b1_sci.fit
Why are I values biased by -120?

## Slide 22: CONCLUSIONS — 1 of 2
Both raw and calibrated data can be extracted using only
  Documentation,
  PDS labels, and
  Practice
  No FITS or other tools or code fragments were used
ROF, unpacked, and calibrated data are consistent
Successfully concatenated files to show entire sequences during Pluto encounter

## Slide 23: CONCLUSIONS— 2 of 2
DSN signal is within passband during encounter, so occultation analysis should be possible
SNR of DSN signal is in expected range
Beginning of occultation chord is well-defined in SNR
Pluto is visible in day and night side radiometer scans

## Slide 24: MAIN ISSUES
Largely concerned with the calibration process
Absolute times are uncertain by as much as 1 s in radiometry, I/Q sampling, and conversion using MET-to-UTC table (important for occultation chord derivation)
Absolute amplitude calibration of radiometer is not understood (important for surface temperature estimation)
  Derivation of Tsys is missing steps
  Measurements are non-physical assuming nominal Tsys
Polarization of data is not known
Test data may be puzzling without more explanation

## Slide 25: NOT DONE
Did not study frequency/phase behavior of DSN signal in I/Q sample data (re occultation analysis)
Did not attempt to reconstruct observing geometry
Looked at only a small subset of test data