## Slide 1: Rosetta CIVA PDS Delivery Review
Oct 6 2017

## Slide 2: Summary of Data Under Review
CIVA-P images from the Philae lander
One image from each of the 7 cameras
  CCD cameras. 1024 x 1024
  Same detector as MESSENGER MDIS
Calibrated
  Very large dynamic range
  What are the units?
  Appears valid
Uncalibrated data
  Instrument ICD is provided and provides very useful information describing the calibration steps.
  All calibration files appear to be included; and formatted as described. Based on pre-flight cal.
  Unfortunately, was unable to read in an image to appear like the browse products
    File sizes are unexpected
Calibration Data
  Is present
  However, I have not found how the instrument data is converted from DN to Reflectance.
  Insufficient information on where the instrument is pointed

## Slide 3: CIVA-P
ÇIVA-P is constituted of 7 identical cameras, implemented as 5 single cameras and one stereoscopic pair of two co-aligned ones, thus filling the 360° panoramic field of view by six overlapping FOV of 70° each, 60° apart one from the next (Figure 1). All cameras are mounted at the top of the side panels of the Lander.

## Slide 4: Calibrated Data
Browns image

## Slide 5: Calibrated Data
Stereo pairs
What are these images of?
Values [0, .5, 1]
?

## Slide 6: Uncalibrated Data
Different file sizes
Apparent data drops
What units are these data?
Scattered light & ghosting?
Browse image

## Slide 7
Histogram
(data: 0 to ~6.5e4)
Raw Data
Calibrated Data
Histogram

## Slide 8: RID
There is information pertaining to all the cameras in each of the camera's labels. Including processing steps. it is confusing as two which step was performed on which camera. Are thee various processing steps somehow interdependent between cameras? there are references to 'camera cubes'...is that referring to the imaging spectrometer portion of the instrument?