## Slide 1: PDS Data Review Rosetta NAVCAM
Tony Farnham
Oct 9, 2017

## Slide 2: NAVCAM Instrument
Navigation camera
  2 identical, redundant cameras
  Only CAM1 (NAVCAM-A) was ever used extensively.
  CAM2 (NAVCAM-B) took some test data to make sure it was working.
70 mm, f/2.2 camera
  1024 x 1024 pixels
  17.6 arcsec pixels (5∘ x 5∘ FOV)
  12 bit data

## Slide 3: NAVCAM Datasets
34 Datasets:
  Includes all NAVCAM data obtained throughout the mission
Raw data only
  No calibration information to review
  Documents say radiometric calibration will be done in the future
Datasets are very similar, with most catalog and documents files the same between sets
  Typos in those files apply to all datasets
Data format
  IMG files with detached PDS labels
  FITS files with detached PDS labels
    Under Extras directory
    Not technically part of the archive (It should be)
  JPG browse files
    Very useful for referencing the images

## Slide 4: NAVCAM Data Files
Tested both IMG and FIT files
  Used PDSREAD (IMG and FIT)
  Used IDL FITS readers
  Able to read every image
  16772 by my count
Compared IMG and FIT and found them to be identical
Spot-checked with NASAview (read successfully, but crashed often)
Spot-checked the browse images to confirm if they correspond to the data files
Able to display and manipulate the data
Tried making a movie to show the rotation (didn’t look very good…..)

## Slide 5: Geometry Check
Spot checked the geometry calculations in the labels against my calculations from the Rosetta SPICE data.
Excellent results – everything agrees well

## Slide 6: Liens / RIDs
Note: Did not submit a RID about this issue
Since the FITS files already exist, they should be moved from the Extras directory to the data directory so that they are officially part of the archive
RID Description: FIT files are included in the Extras directory, which is not technically part of the archive. They should be included as data, for those users who prefer FITS format.
Recommended Solution: Move the FIT files to subdirectories in the Data Directory.

## Slide 7: RID NAVCAM-US-TF-001
Various documents and catalog files highlight the context images, but they are never described. It would be useful to have more information on these images as a cross reference to other data sets.
It would be useful to have more information about the images that are not 1024x1024

## Slide 8: Comments about RIDs from Thomas Roatsch
NAVCAM-EU-TR-003 - Boresight values
  The values in the EAICD and the SPICE kernels look consistent to me. (Note that the EAICD values are in the FK, not the IK files as stated). Or am I missing which values are being compared?
NAVCAM-EU-TR-005 - LINE DISPLAY DIRECTION
  I disagree with this one. Having the orientation defined is a good thing because it takes out ambiguity. Many software routines use “DOWN” but others use “UP”. The user needs to be aware of what is assumed if the software ignores the keyword.

## Slide 9: Comments about RIDs from Thomas Roatsch
NAVCAM-EU-TR-006 - Reference body is not described
  Not sure if this is relevant. There are multiple DSK shape models available, and I don’t think anything in the dataset is dependent on which one is used. Only dependent on the coordinate system
NAVCAM-EU-TR-008 - Missing info about lost rows/images
  I agree with this. It would be good to have some sort of introduction of lost rows and what causes them. Also, noting the lost images is meaningless if there is not a list of the scheduled images.
NAVCAM-EU-TR-009 - Geometry Index file missing
  I agree with this. Would like to see a searchable geometry index file.

## Slide 10: Typos
Numerous typos and errors in various files
  Submitted separately to the editorial inputs

## Slide 11: Summary
Data sets are in excellent shape
  No major issues of any kind
  A few minor concerns and items that would be useful to add
  Quite a few typos
Data are certifiable