## Slide 1: MIRO PDS review July 2018
Martin Cordiner
CUA / NASA GSFC

## Slide 2: MIRO (Microwave Instrument for Rosetta Orbiter)
First microwave instrument sent to study a Solar System body
Combined ultra high-resolution heterodyne spectrometer, and radiometer
Two wavebands: 190 GHz (1.6 mm) and 562 GHz (0.5 mm)
Single-pixel sub-mm receiver with beam size 7.5’
Sensitive to thermal emission as well as ground-state spectral lines from H2O and NH3
Can detect CO and CH3OH

## Slide 3: The Data
Simultaneous 1.6 mm and 0.5 mm continuum and spectroscopy of the region 556-580 GHz (divided into 8 spectral windows)
Frequency-switched spectra with integration time 30 s

## Slide 4: Average of 1000 H2O spectra on UT2014-12-13
Level 3 data product
ro-c-miro-3-esc1-67p-v3.0

## Slide 5: Converting IF to Sky frequency

## Slide 6: Level 4 ‘folded’ H2O spectrum
Tdv ~ 70 K km/s  N(H2O) ~ 1014 cm-2 (at 100 K)

## Slide 7: Time series H2O

## Slide 8: MIRO spatial scans

## Slide 9
Continuous sequence of spectra over ~ 5 min period
Angle between comet and boresight obtained from geometry file
Comet-MIRO distance = 19.2 km
-> r = 0.13 km cf. comet size of ~ 2 km
Shape model (FOUND_INTERSECTION = 1) indicates we are still inside the geometrical limits of the comet

## Slide 10
H218O
CH3OH
NH3

## Slide 11: Review summary
  + Documentation is complete, comprehensive and well written
  + Data can be understood without external documentation
  + Calibration process is explained in sufficient detail
  + Data labeling is comprehensive
  + Python routine is provided for data access
  Documentation file names could be more descriptive
  Abbr. “S/C” on p1 of “ro_mir_if_0001.pdf” not defined
  Label description typo in geom_level_4_format.fmt: "Doppler shift velocities” --> "Doppler shifted"?
  Meaning of data versions (ver-1.0, 2.0, 3.0) not described
  Each dataset could benefit from a description/summary. What does it contain? Could be useful for someone not familiar with the CODMAC levels or mission phases (although these are detailed in ro_mir_if_0001.pdf)
  Rest frequencies of the individual spectral windows are not given (or not obvious to me). I believe these are required for a full analysis
  Python routine needs to give easier access to individual data columns (very tedious to separate spectral arrays from the binary stream)
  Python routine does not work on case-sensitive (ie. most) file systems