## Slide 1: PDS Review Rosetta RPC-ICA
Yaxue Dong
CU-Boulder/LASP
University of Maryland, College Park, MD
Oct 8-9, 2018

## Slide 2: Overview
ro-c-rpcica-5-ext1-moment-v1.0
  Rosetta Plasma Consortium – Ion Composition Analyzer
  Extension 1: Jan 01 2016 to Apr 5 2016
  L5 data: ion moments (density and velocity)
No description for the generation of L5 data
“rpc_user_guide.pdf” cannot be opened (damaged file)

## Slide 3: Read the data
Tools:
  PDS3 IDL software: works well
  Provided MatLab software: only works for label files and lower level of data

## Slide 4: Data Structure
SPACECRAFT EVENT TIME UTC
MASS
CHARGE
DENSITY
VX
VY
VZ
DURATION
QUALITY FLAGS

## Slide 5
Quality flag description
1 or 0 ?

## Slide 6: Plot the data
Separated by mass/charge
  1/1: H+
  4/2: He++
  4/1: He+
  18/1: H2O+, other water group ions? O+? (should be in L5 data description)
H+, He++, He+ ?

## Slide 7
Close to the comet
Alt ~12 km
Dominated by heavy ions
n (cm-3)
V (km/s)
n (cm-3)
V (km/s)
n (cm-3)
V (km/s)
n (cm-3)
V(km/s)
m/q = 1/1
m/q = 4/2
m/q = 4/1
m/q = 18/1

## Slide 8
Far away from the comet
Alt >900 km
Dominated by solar wind protons
n (cm-3)
V (km/s)
n (cm-3)
V (km/s)
n (cm-3)
V (km/s)
n (cm-3)
V(km/s)
m/q = 1/1
m/q = 4/2
m/q = 4/1
m/q = 18/1

## Slide 9: Summary
Generally the data looks great.
Only one major RID:
  No description for the generation of L5 data: Please add descriptions or provide a reference.
Minor RID:
  “rpc_user_guide.pdf” does not open correctly
  Unclear data quality flag description
  The provided MatLab software only works for lower level data and label files
Editorial:
  “areadme.txt”: “solar wind ions (H+,H2+,He+)”  “(H+, He++, He+)”