## Slide 1: PDS Data Review New Horizons LORRI & MVIC
Tony Farnham
Sept 5, 2019

## Slide 2: General comments
Many of the files are common between all LORRI and MVIC datasets. Highlight the problems of those files here, and liens should propagate to all data sets.
Additional comments are given on files that are specific to individual data sets.

## Slide 3: MVIC - RAW and CAL

## Slide 4: MVIC Instrument
Part of the RALPH instrument
PanFrame CCD
  5024x128 pixels sweep over the scene
  128 pixels per exposure time
  Create an image cube 5024 x 128 x XXX pixels, where XXX is defined by scan rate and time
  Not clear how these data are used, though there are not many of them
Six other CCDs operate in TDI mode (different filters)
  5024x32 pixels sweep over the scene
  The 32 pixels are clocked at the scan rate, so each exposure time gives a shift of 1 pixel
  Creates an image 5024 x XXX
Raw data format
  FITS files with 3 extensions
    Primary image, housekeeping, window mismatch table
Calibrated data format
  FITS files with 3 extensions
    Primary image (DN), Error map, Quality flag image
    Do-it-yourself flux calibration: Flux conversion coefficients are added to the header

## Slide 5: General Comments
Data from Aug 2018 – Dec 2018
Four datasets:
  KEM Cruise phase , V2.0, Raw and calibrated (11 image cubes)
    21 Sep 2017 – 13 Jul 2018
  KEM1 Encounter phase, V1.0, Raw and calibrated (19 images)
    30 Aug 2018 – 30 Dec 2018
Very similar, with many files the same
Overall, all data sets are in great shape
Well documented with lots of description and information available

## Slide 6: Catalog Files
DATASET.CAT
  Typo (LORRI and MVIC)
  "This indicates either that the target was either a star, or that the ...” --> "This indicates that the target was either a star, or that the ..."

## Slide 7: SPICE
DATASET.CAT file states that the dataset used to compute geometry is NH-X-SPICE-6-PLUTO-V1.0
Dataset available from NAIF is NH-J/P/SS-SPICE-6-V1.0
  Coverage ends before this dataset starts
  Couldn’t find a more updated set of kernels
Can’t check the geometry in the headers and labels without updated kernels
  Previous reviews have identified occasional issues, but geometry was good for the most part
Does the SPICE dataset ID in the DATASET.CAT file need updated?
Relevant to both the MVIC and LORRI data

## Slide 8: MVIC Data Files – RAW and CAL
Data are in good shape
  Read with IDL FITS readers, PDSREAD and NASAView
  Includes extensions
  Read and displayed every image
  Tested to make sure data could be manipulated and measured

## Slide 9: MVIC Status
A few minor changes to documents and labels
Status of SPICE / geometry is unknown
Data are Certifiable

## Slide 10: LORRI - RAW and CAL

## Slide 11: LORRI Instrument
Narrow angle, panchromatic camera
  0.29 degree square FOV
  High resolution (5 microradian/pixel)
  1024x1024 pixel CCD detector
  Operates in 1x1 or 4x4 on-chip binning modes
Raw data format
  FITS files with 5 extensions
    Primary image, Histogram, First 34 pixels, Image descriptor, Window mismatches
Calibrated data format
  FITS files with 3 extensions
    Primary image (DN), Error map, Quality flag image
    Do-it-yourself flux calibration: Radiance and Irradiance calibration coefficients are given in the header

## Slide 12: General Comments
Four Datasets:
  KEM Cruise phase, V2.0, Raw and Calibrated (1863 images)
    28 Jan 2017 – 6 Dec 2018
  KEM1 Encounter phase, V1.0, Raw and Calibrated (1648 images)
    15 Aug 2018 – 31 Dec 2018
Very similar, with many files the same
Overall, all data sets are in great shape
Well documented with lots of description and information available
Comments noted above apply to LORRI

## Slide 13: Various
DATASET.CAT
  Some of the text refers to the MU69 event in the future tense
  May be other occurrences
  Should be changed to past tense for consistency throughout

## Slide 14: Data
Data are in good shape
  Read with IDL FITS readers, PDSREAD and NASAView
  Includes extensions
  Read and displayed every image
  Tested to make sure data could be manipulated and measured

## Slide 15: Data
One partially bad image
  nh-x-lorri-2-kem1-v1.0/data/20181121_040511/lor_0405118588_0x633_eng.fit
  nh-x-lorri-3-kem1-v1.0/data/20181121_040511/lor_0405118588_0x633_eng.fit
  Does a good version exist?

## Slide 16: LORRI Status
A few minor changes to documents and labels
Status of SPICE / geometry is unknown
Data are Certifiable