## Slide 1: PDS Data Review New Horizons LORRI & MVIC
Tony Farnham
Feb 27, 2020

## Slide 2: LORRI - RAW and CAL

## Slide 3: LORRI Instrument
Narrow angle, panchromatic camera
  0.29 degree square FOV
  High resolution (5 μrad/pixel)
  1024x1024 pixel CCD detector
  Operates in 1x1 or 4x4 on-chip binning modes
Raw data format
  FITS files with 5 extensions
    Primary image, Histogram, First 34 pixels, Image descriptor, Window mismatches
Calibrated data format
  FITS files with 3 extensions
    Primary image (DN), Error map, Quality flag image
    Do-it-yourself flux calibration: Radiance and Irradiance calibration coefficients are given in the header

## Slide 4: General Comments
Two Datasets:
  KEM1 Encounter phase, V2.0, Raw and Calibrated (2119 images)
    15 Aug 2018 – 05 Jan 2019
Extends the date over V1.0 by a few days
  Fills in additional downloaded data
  Adds images of 2014 MU69
Overall, both data sets are in great shape
Well documented with lots of description and information available

## Slide 5: Various
DATASET.CAT
  Misleading line (minor issue)
    Suggested change “This mission phase includes data… This version of the dataset includes only data downlinked….”
  Added: Reference to 0.6 ms exposure time change
    This should be documented somewhere (here? new document?)
    Why was this done? When was it applied, etc.

## Slide 6: Data
Data are in good shape
  Read with IDL FITS readers, PDSREAD and NASAView
  Includes extensions
  Read and displayed every image
  Tested to make sure data could be manipulated and measured
One-to-one correspondence between raw and calibrated files

## Slide 7: SPICE
DATASET.CAT file states that the dataset used to compute geometry is NH-J/P/SS-SPICE-6-V1.0.
Dataset is available from NAIF
  Coverage ends before this dataset starts (2016)
  Couldn’t find a more updated set of kernels
Can’t check the geometry in the headers and labels without updated kernels
  Previous reviews have identified occasional issues, but geometry was good for the most part
Relevant to both the LORRI and MVIC data

## Slide 8: LORRI Status
A couple minor changes to DATASET.CAT file
  Possibly add a document describing the change in exposure time
Status of SPICE / geometry is unknown
Data are Certifiable

## Slide 9: MVIC - RAW and CAL

## Slide 10: MVIC Instrument
Part of the RALPH instrument
PanFrame CCD
  5024x128 pixels sweep over the scene
  128 pixels per exposure time
  Create an image cube 5024 x 128 x XXX pixels, where XXX is defined by scan rate and time
  Not clear how these data are used, though there are not many of them
Six other CCDs operate in TDI mode (different filters)
  5024x32 pixels sweep over the scene
  The 32 pixels are clocked at the scan rate, so each exposure time gives a shift of 1 pixel
  Creates an image 5024 x XXX
Raw data format
  FITS files with 3 extensions
    Primary image, housekeeping, window mismatch table
Calibrated data format
  FITS files with 3 extensions
    Primary image (DN), Error map, Quality flag image
    Do-it-yourself flux calibration: Flux conversion coefficients are added to the header

## Slide 11: General Comments
Two datasets:
  KEM1 Encounter phase, V2.0, Raw and calibrated (77 images)
    30 Aug 2018 – 01 Jan 2019
Extends the date over V1.0 by one day
  Adds additional downloaded data
  Adds images of 2014 MU69
Overall, both data sets are in great shape
Well documented with lots of description and information available

## Slide 12: Catalog Files
DATASET.CAT
  Misleading line
    Suggested change “This mission phase includes data… This version of the dataset includes only data downlinked….”

## Slide 13: MVIC Data Files – RAW and CAL
Data are in good shape
  Read with IDL FITS readers, PDSREAD and NASAView
  Includes extensions
  Read and displayed every image (caveat on next slide)
  Tested to make sure data could be manipulated and measured
One-to-one correspondence between raw and calibrated files

## Slide 14: MVIC Problem File
Dataset nh-a-mvic-2-kem1-v2.0
File mp2_0408625963_0x530_eng.lbl
  ^IMAGE pointer is missing
  Different from other images (5024 x 36336 pixels)
  The filesize is appropriately large and the calibrated version of the file exists, so the data must be available

## Slide 15: MVIC Problem File
Dataset nh-a-mvic-3-kem1-v2.0
File mp2_0408625963_0x530_sci.lbl
  Same file as in the raw data
  The image is readable, but the ^EXTENSION_QUALITY_IMAGE pointer is missing

## Slide 16: MVIC Status
A minor change in DATASET.CAT file
  One image (both raw and calibrated) needs fixing
Status of SPICE / geometry is unknown
Data are Certifiable

## Slide 18: General comments
Many of the files are common between all LORRI and MVIC datasets. Highlight the problems of those files here, and liens should propagate to all data sets.
Additional comments are given on files that are specific to individual data sets.