## Slide 1: Rosetta OSIRIS Sample Dataset GEOSPICE
Jian-Yang Li
Planetary Science Institute
8/4/2020

## Slide 2: Overview
Datasets: ro-c-[osinac/osiwac]-5-esc1-67p-m12-geospice-v0.1
OSIRIS Level 5 georeferenced images in MPT 12, collected from between 2015-01-13T23:25:00 and 2015-02-10T23:24:59
Improved georeferenced data ‘geo’ version previously released, intended to replace the ‘geo’ version
Changes from ‘geo’ version
  Improved registration between image and backplanes with automated shift using cross-correlation
  Use of 2M shap7 rather than 4M shap7 shape model
  Improved NAC bad column 995
  Improved WAC distortion correction
  Improved boresight correction with dependent on filter and temperature
  Bug fixes: boresight center for enlarged frame
  Some updates in PDS headers
  Updated documents: OSIRIS_SIS_V08 (from v05), SCIENCE_USER_GUIDE_V07 (from v03), OSIRIS_CAL_PIPELINE_V10 (from v06)
Overall excellent datasets almost free of problem

## Slide 3: Review steps
Checked dataset.cat files, with comparison with the corresponding ‘geo’ version
Checked all documents in document/ directory
  Primarily osiris_eaicd_v08.pdf, science_user_guide_v07.pdf, osiris_sis_v08.pdf, and osiris_cal_pipeline_v10.pdf, as well as geo_products_v03.pdf in documents/calib/
Review image data
  Load with various software, compare IMG
  Compare the original frame size and enlarged frame size for the center part, as well as PDS headers
  Compare with upstream level, particularly the ’geometric distortion corrected flux’ images to check whether the the processing is consistent with previous version
Did NOT do
  Check the catalog files that are common in previously released datasets
  Check calibration data files
  Run calibration pipeline
  Check index/ directory

## Slide 4: Catalog and Documentation
Overall similar to the catalog files in ‘geo’ version, except for the updated information to reflect the new ‘geospice’ version
Suggestion: The difference between ‘geospice’ and the previously released ‘geo’ should be briefly outlined in the dataset catalog file, and a pointer should be provided to reference the relevant documentation files. In particular:
  The improved registration of backplanes with auto shift is very important from the point of view of users and should be explicitly mentioned
  The difference in the shape model used should be explicitly mentioned and the reason should be given
  A brief list of other small improvements will be useful
Complete and excellent documentation included
Correction for geo_products_v03.pdf: In page 6, “…(file mask ID and FF)…” should be “…ID and EF…”

## Slide 5: Images
All images can be load with IDL readpds, and my own Python code
The overlapping part of the original size frame and enlarged frame are identical, except for one line of the image near the upper edge that appear to be due to interpolation of images in distortion correction near the frame edge
Verified with a few randomly selected images that the total flux of image layer is consistent with that measured from previously released flux image
No any problem identified
Seems like ‘geospice’ version includes 20 more images than ‘geo’ version for NAC, and 67 more images for WAC. Why the difference? Is it worth pointing out somewhere (e.g., dataset.cat)?

## Slide 6: Summary
Overall excellent datasets almost free of problems
Liens
  Add information about the improvement/difference of this ‘geospice’ version from the previously released ‘geo’ version
  Correct one place in geo_products_v03.pdf: Page 6, “FF” should be “EF”
  Explain the difference in images included between ‘geospice’ version and ‘geo’ version
Can be certified