## Slide 1: PDS-SBN Review of New Horizons LEISA Data (2014 MU69 Flyby Approach)
M. DiSanti
04 Dec 2020

## Slide 2
A spatial-spectral data cube is created by scanning the FOV across the target in a “push-broom” fashion. The data cube is a 3-dimensional array having 256x256xN elements, where N is the number of 256x256 files accumulated over the scan.
e.g., read in calibrated FITS file = ‘nh-p-leisa-3-pluto-v2.0/data/20150714_029917/lsb_0299172889_0x53c_sci.fit’
file = file(x,y,z),
x=spatial (256 elements),
y=lambda(256 elements),
z=spectral/spatial
(N=elements; e.g., N=371)
(i.e., lambda varies spatially)
[figure from ‘leisa_data.pdf’ in
folder ‘document’]

## Slide 3: LEISA
A near-IR (1.2 – 2.5 micron) spectrometer that uses a 256x256 Rockwell PICNIC array, with 40-micron square pixels.
It produces low-resolution (l/Dl ~ 240) and higher-resolution (l/Dl ~ 540) spectra over separate sections (ranges of 54 and 199 rows) that are separated by 4 rows obscured by a bond joint.
Note: “Hi-res” l/Dl was ~ 425 for Pluto flyby data (as below) but is ~ 540 for cruise & 2014 MU69 approach phases (recalibration)

## Slide 4
LEISA Wavelength Calibration
lambda
Delta-lambda
(x 100)
Lambda / Delta-lambda
v3.0
v4.0

## Slide 5
Transpose file(x,y,z) [256,256,N]  file_tr(x,z,y) [256,N,256]
file(0:255,0:N-1,0)
file(0:255,0:N-1,127)
file(0:255,0:N-1,255)

shift -
register
file_tr_sh(0:255,0:N-1,S[0:255])
(i.e., summed over all lambdas)
(Some residual wobble in x-dim)
LEISA Pluto flyby Data

## Slide 6
Arrokoth (2014 MU69) Approach
“First Look” at MU69, at
d~106 km (with LORRI)

## Slide 7
DATA

## Slide 8
LEISA CRUISE DATA (20aug2018)
/data/20180820_039709/lsb_0397097519_0x53c_eng.fit (Alpha Lyrae)
Channel 9 (2.4088 mm)
Channel 250 (2.1038 mm)
Channel 194 (1.2384 mm)
Low-res (l/Dl ~ 243)
High-res (l/Dl ~ 542)
|<-------------------------------------------------------------------------------->|
(Spatially unregistered)

## Slide 9
LEISA CRUISE DATA (20aug2018)
/data/20180820_039709/lsb_0397097519_0x53c_eng.fit (Alpha Lyrae)
Channel 9 (2.4088 mm)
Channel 250 (2.1038 mm)
Channel 194 (1.2384 mm)
Low-res (l/Dl ~ 243)
High-res (l/Dl ~ 542)
|<-------------------------------------------------------------------------------->|
(Spatially registered)

## Slide 10
LEISA approaching MU69 (01jan2019)
lsb_0408624418_0x53c_eng.fit (04:50 – 05:05 UT), <d> = 31.2e3 km
Ch255
(high_res2.0895 mm)
Ch1
(low_res2.4744 mm)
Spatially
Unregistered
(Raw)
End: row173
Start: row392 
Ch127
(low_res1.5748 mm)
Mid: row290 
Subtract median
at each step in l

## Slide 11
LEISA approaching MU69 (01jan2019)
lsb_0408624418_0x53c_eng.fit (04:50 – 05:05 UT), <d> = 31.2e3 km
Ch255
(high_res2.0895 mm)
Ch1
(low_res2.4744 mm)
Spatially
Registered
(Raw)
 Row173
Start: row392 
Ch127
(low_res1. mm)
Mid: row290 

## Slide 12
LEISA approaching MU69 (31dec2018/01jan2019)
lsb_04086*_0x53c_eng.fit near 2.1 µm (~ channel 50)
* = 05304
(3.06e5 km)
* = 14341
(1.75e5 km)
* = 19338
(1.04e5 km)
* = 21929
(6.55e4 km)
* = 24118
(3.12e4 km)

## Slide 13
20190101_042999 (01jan2019, “calibrator” files)
“Sun” (row 8)
“Sun” – dark
(0759-1259)
dark (row 8)
(1259)

## Slide 14
LEISA Wavelength Calibration
lambda
Delta-lambda
(x 100)
Lambda / Delta-lambda
v3.0
v4.0

## Slide 15
LEISA Intensity Calibration
Row10
Row230
Row50
Row127
Row199
Could express as flux density,
e.g., Rayleighs/Angstrom
(106 ph s-1 cm-2 A-1)
once aperture (e.g., pixel) angular subtense is specified. The pixel solid angle Omega(pix) 1.7e-7 sr (taken from ‘calinfo.txt’).


## Slide 16
Summary/Suggestions (v4.0)
LEISA frames read in fine, for both raw and calibrated) data.
lambda 2.5-1.225um (rows0 thru 199, low res), 2.25-2.10um (rows204 thru 255, hi res).
In v4.0, asteroid Arrokoth (2014 MU69) is clearly detected from 3.06e5 km inward, but files from 4.10e5 and 1.21e6 km contain all zeroes.
MU69 scan direction is “upward” for d = 1.04e5 km and larger. In each case it was ~1 row per step in l. But it’s still downward for 6.55e4 and 3.12e4 km. Please check.
One file has ‘54b’ instead of ‘53c’ in its name. (20190101_040861/lsb_0408611759_0x54b_eng.fit’) Is this intentional?
Files 20190101_042999/* have only 16 rows. The first one (“Sun”) looks more like an internal lamp (flat field?). The second file (“dark”) looks reasonable.
Spatial Registration
Both Vega and MU69 data show some “wobble” in the x-direction, more so for Vega, less so for MU69 , especially in “closer” files (6.55e4 km, 3.13e4 km). Arcturus files look weird from
Difficult to extract spectra for Vega, Arcturus, and MU69, due to spatial smearing (not so critical for Pluto). Arcturus files have less “wobble.” This should be less important for MU69 near closest flyby approach of ~3500 km. Arcturus looks better in ‘calibrated’ data.
In ‘calinfo.txt’: pixel solid angle is denoted ‘aOmega’, but that is normally expressed as entendue (m^2 sr). This was not changed from v3.0, but this is a trivial distinction anyway. The typo flagged in the v3.0 review (“intergration time”) was addressed.
STILL looking forward to seeing the actual MU69 flyby data!

## Slide 17
DATA