## Slide 1: DART/DRACO Sample Dataset
Jian-Yang Li
Planetary Science Institute
7/16/2021

## Slide 2: Overview
Sample dataset of DART/DRACO images
Dataset content
  240 DRACO images from the “final” phase, with processing levels of both “raw” and “calibrated”, and 4 backplane data “derived”
  Images and backplanes are stored in FITS format, with accompanying PDS4 .xml labels and .png images
  Calibration reference data
  Documentation includes a SIS document and a calibration pipeline description in PDF format, as well as some high-level overview file in plain text (.txt)
Overall assessment
  Good documentation, easy to follow, with comprehensive information
  Image labels appear to be sufficient to understand and use the data
  Some minor problems in the documentation. Missing keywords in FITS headers.

## Slide 3: Documentation
jhuapl_dart_draco_calibration_pipeline_descxription_210315.pdf
  Page 9, first few lines: calibration pipeline input file directory ‘cal_files/’ and subdirectory structure described here are different from the directory structure in the data bundle. -- minor inconsistency
  Last page, FITS keyword IFOV is missing in calibrated images, and not included in the SIS doc
jhuapl_dart_draco_uncalibrated_calibrated_sis_210626.pdf
  Page 12, section 4.1.3: “DRACO typically employs high gain, 30x when operating in rolling shutter mode to maximize the SNR”. I though high gain is to utilize full-well capacity, while low gain is to maximize SNR. -- minor confusion
Some repetitive information in each of both documents can be removed to avoid potential conflict and simplify reading. E.g., raw image format is “single HDU, 1024 x 1024, 32-bit floating point FITS, 2x2 binned from the original 2048 x 2048 window1…” appears a few times in an identical form. -- minor suggestion
Question
  SIS document, page 20, section 4.3.3: Does this section apply to lightcurve data (which is not included in this sample data)?

## Slide 4: Images
No problems found
All images can be loaded and displayed with astropy.io.fits and DS9. pds4_tools.view also works for a subset of images manually checked
Display direction correctly defined and consistent with the description in documentation
I didn’t check the reasonableness of pixel values

## Slide 5: FITS header keywords
No problems found
All information that is potentially useful for data processing and analysis are included in the FITS headers, some propagate to PDF4 labels
The geometry values appear to be calculated from DRM kernels and reasonable
The SMART Nav key values seem to be filled rather than derived, because the positions of Didymos and Dimorphos and other values are all the same in all images, even though the two objects appear to be separating from each other as the spacecraft moves closer

## Slide 6: Calibration data
All calibration data described in the calibration doc exist in sub-directory calibration/
Radiometric calibration lookup table .csv file contains header information commented by hashtag (#), therefore it cannot be directly opened by MS Excel, but no problem with other more generic tools such as `astropy.io.ascii`. Should this be noted somewhere, maybe in the calibration doc? -- very minor suggestion

## Slide 7: Conclusion
A well-prepared dataset with all required information and documentation available and clearly described
No major problems, some minor fixes or revisions are suggested

## Slide 8: Typos
readme.txt
  Line 17, something seems to be missing in “See these resources in the [ ] for more information”
Pipeline doc
  Page 13: REFDKAR2  REFDARK2
SIS doc
  Page 13, third line from bottom: an extra ` in “spacecraft`”
  Page 18, last sentence in the first paragraph of section 4.3.2.2: “… are included in the as part of”, remove “in the”