## Slide 1: PDS-SBN Review of New Horizons LEISA v5.0 Data (2014 MU69 Approach)
M. DiSanti
10 Feb 2022

## Slide 2
A spatial-spectral data cube is created by scanning the FOV across the target in a “push-broom” fashion. The data cube is a 3-dimensional array having 256x256xN elements, where N is the number of 256x256 files accumulated over the scan.
e.g., read in calibrated FITS file = ‘nh-p-leisa-3-pluto-v2.0/data/20150714_029917/lsb_0299172889_0x53c_sci.fit’
file = file(x,y,z),
x=spatial (256 elements),
y=lambda(256 elements),
z=spectral/spatial
(N=elements; e.g., N=371)
(i.e., lambda varies spatially)
[figure from ‘leisa_data.pdf’ in
folder ‘document’]

## Slide 3: LEISA
A near-IR (1.2 – 2.5 micron) spectrometer that uses a 256x256 Rockwell PICNIC array, with 40-micron square pixels.
It produces low-resolution (l/Dl ~ 240) and higher-resolution (l/Dl ~ 540) spectra over separate sections (ranges of 54 and 199 rows) that are separated by 4 rows obscured by a bond joint.
Note: “Hi-res” l/Dl was ~ 425 for Pluto flyby data (as below) but is ~ 540 for cruise & 2014 MU69 approach phases (recalibration)

## Slide 4
LEISA Wavelength Calibration
lambda
Delta-lambda x 100
Lambda / Delta-lambda

## Slide 5
Arrokoth (2014 MU69) Approach
“First Look” at MU69, at
d~106 km (with LORRI)

## Slide 6
LEISA CRUISE DATA (20aug2018)
/data/20180820_039709/lsb_0397097519_0x53c_eng.fit (Alpha Lyrae)
Channel 9 (2.4088 mm)
Channel 250 (2.1038 mm)
Channel 194 (1.2384 mm)
Low-res (l/Dl ~ 243)
High-res (l/Dl ~ 542)
|<-------------------------------------------------------------------------------->|
(Spatially unregistered)

## Slide 7
LEISA CRUISE DATA (20aug2018)
/data/20180820_039709/lsb_0397097519_0x53c_eng.fit (Alpha Lyrae)
Channel 9 (2.4088 mm)
Channel 250 (2.1038 mm)
Channel 194 (1.2384 mm)
Low-res (l/Dl ~ 243)
High-res (l/Dl ~ 542)
|<-------------------------------------------------------------------------------->|
(Spatially registered)

## Slide 8
LEISA MU69 Approach DATA

## Slide 9
LEISA approaching MU69 (01jan2019)
lsb_0408624418_0x53c_eng.fit (04:50 – 05:05 UT), <d> = 31.2e3 km
Ch255
(high_res2.0895 mm)
Ch1
(low_res2.4744 mm)
Spatially
Unregistered
(Raw)
End: row173
Start: row392 
Ch127
(low_res1.5748 mm)
Mid: row290 
Subtract median
at each step in l

## Slide 10
LEISA approaching MU69 (01jan2019)
lsb_0408624418_0x53c_eng.fit (04:50 – 05:05 UT), <d> = 31.2e3 km
Ch255
(high_res2.0895 mm)
Ch1
(low_res2.4744 mm)
Spatially
Registered
(Raw)
 Row173
Start: row392 
Ch127
(low_res1.5748 mm)
Mid: row290 

## Slide 11
LEISA approaching MU69 (01jan2019)
lsb_0408624418_0x53c_sci.fit (calibrated), <d> = 31.2e3 km
Ch10
(low_res2.4004 mm)
Ch255
(high_res2.0895 mm)
Ch127
(low_res1.5748 mm)

## Slide 12
LEISA approaching MU69 (01jan2019)
lsb_0408621929_0x53c_sci.fit (calibrated), <d> = 65.5e3 km
Ch10
(low_res2.4004 mm)
Ch255
(high_res2.0895 mm)
Ch127
(low_res1.5748 mm)

## Slide 13
lsb_0408619338_0x53c_sci.fit (calibrated), <d> = 104e3 km
Ch10
(low_res2.4004 mm)
Ch225
(high_res2.1795 mm)
Ch127
(low_res1.5748 mm)
lsb_0408614341_0x53c_sci.fit (calibrated), <d> = 175e3 km







## Slide 14
LEISA approaching MU69 (01jan2019)
lsb_0408613050_0x53c_sci.fit (calibrated), <d> = 1.94e5 km
Ch10
(low_res2.4004 mm)
Ch190
(high_res1.2552 mm)
Ch127
(low_res1.5748 mm)




## Slide 15
LEISA approaching MU69 (01jan2019)
lsb_0408610468_0x53c_sci.fit (calibrated), <d> = 2.32e5 km
Ch10
(low_res2.4004 mm)
Ch190
(high_res1.2552 mm)
Ch127
(low_res1.5748 mm)




## Slide 16
LEISA approaching MU69
lsb_0408609177_0x53c_sci.fit (calibrated), <d> = 2.50e5 km (01jan2019)
Ch10
(low_res2.4004 mm)
Ch190
(high_res1.2552 mm)
Ch127
(low_res1.5748 mm)
lsb_0408606595_0x53c_sci.fit (calibrated), <d> = 2.88e5 km (31dec/01jan)
 (?)
 (?)
 (?)
 (?)
 (?)
 (?)

## Slide 17
LEISA approaching MU69 (31dec2019)
lsb_0408605304_0x53c_sci.fit (calibrated), <d> = 3.06e5 km
Ch10
(low_res2.4004 mm)
Ch190
(high_res1.2552 mm)
Ch127
(low_res1.5748 mm)



 (??)
 (??)
 (??)

## Slide 18
LEISA approaching MU69 (31dec2019)
lsb_0408542761_0x53c_sci.fit (calibrated), <d> = 1.21e6 km
Ch10
(low_res2.4004 mm)
Ch190
(high_res1.2552 mm)
Ch127
(low_res1.5748 mm)
This data cube appears to be a flat field…

## Slide 19
LEISA MU69 Approach DATA

## Slide 20
LEISA Intensity Calibration
Row10
Row230
Row50
Row127
Row199
Could express as flux density,
e.g., Rayleighs/Angstrom
(106 ph s-1 cm-2 A-1)
once aperture (e.g., pixel) angular subtense given by solid angle Omega(pix) 1.7e-7 sr; fr. ‘calinfo.txt’


## Slide 21
LEISA Intensity Calibration
Could express as flux density,
e.g., Rayleighs/Angstrom
(106 ph s-1 cm-2 A-1)
once aperture (e.g., pixel) angular subtense given by solid angle Omega(pix) 1.7e-7 sr; fr. ‘calinfo.txt’
Raw: 393.0 DN in im127_net(61,156), or 256.6 DN/s if “cadence” = 1.52s
Calibrated: 0.0091637 erg/s/cm^2/A/sr in im127_net(61,156)
Above curve => 12.4090 ph/s at step 127
(lambda 1.57477 um, Dlam 0.00714018 µm)
Pixel solid angle = 1.70d-7 sr
256.6 x 1.7d-7 / Dlam = 6.156e-3 (vs 9.164d-3)
Raw Calibrated
I also tried the per-pixel calibration formula in ‘calinfo.txt’:
C = (((S - E ) / F ) - O ) * G / (I * W * aOmega * gCorr), but I get a ridiculously large number (O(10^12!) so… ?
i i i i i i i
20180820_039709 | lsb_0397097519 | 2018-08-20 | 19:00:01 | 19:07:44 | Vega

## Slide 22
Summary/Suggestions
LEISA frames read in fine, for both raw and calibrated) data.
lambda 2.5-1.225um (rows0 thru 199, low res), 2.25-2.10um (rows204 thru 255, hi res).
Asteroid Arrokoth (2014 MU69) is clearly seen at 65.5e3 and 31.2e3 km, detected to 1.94e5 km. Suggestive at 2.32e5, 2.88e5 (?), and 3.06e5 km (??). Data at 1.21e6 km looks like a flat field (or some such).
While Vega scan direction is “as expected” (target moved upward through lambda, as w/ Pluto scans), MU69 scan direction is reversed (target moved downward through lambda). In each case it was ~1 row per step in l; software was modified to accommodate this.
Spatial Registration
Both Vega and MU69 data show some “wobble” in the x-direction, more so for Vega, less so for MU69.
Difficult to extract spectra for Vega or MU69, due to spatial smearing (not so critical for previous Pluto scans).
I tried to reproduce flux calibration (raw  calibrated data) but was so far unsuccessful.