## Slide 1: Review of Rosetta ROSINA DFMS Time Series Abundances Data
Yinsi Shou
Univ. of Michigan
May 13, 2022

## Slide 2
Does the dataset contain all documentation needed to use and understand its data without prior knowledge?
Yes.
Is the provided documentation well organized, clear and self-consistent?
Yes.
Can the dataset be understood without any external documentation it references?
Yes.
Documentation

## Slide 3: Question
The name of the data set is “Rosetta ROSINA DFMS Time Series Abundances”.
In xml files, the name of the data column is “area under mass peak” with descriptions “Area under the peak corresponding to species H2O. Derived by integrating under the Gaussian(s) fitted to the high-resolution mass peak of species H2O.”
Is it possible to add that “area under mass peak“ is equivalent to “abundance of species X”?

## Slide 4
Plot of “area under mass peak” from XXX_a.tab and XXX_b.tab. (Sep 2014 to Sep 2016)
Plot of ROSINA/DFMS number density currently on PDS/SBN.
Similar trend to the abundance data.

## Slide 5
Plot of the ratio of the linearly interpolated abundance data to abundance data. The interpolation uses two closest abundance data points in time to the timestamps of each density point.
Area under mass peaks (ions in 20 sec) ~ neutral particle flux
Number density (/m^3)
Flux /Number density ~ neutral gas velocity (100 m/s ~ 1 km/s)
The variation of the ratio is expected to be about one order of magntitude.

## Slide 9
The ratios spread wider near the end.

## Slide 11
The ratio of Row b has a wider range than Row a towards the end.

## Slide 13
It seems Row a has a higher quality for C2H6.

## Slide 20
No DFMS number density data available for N2.

## Slide 21
If the assumptions for gas velocities are the same for each species, the abundance to density ratios for each species should also be similar. The variations in the CO data is larger than expected, which may indicate CO data is more difficult to calibrate.

## Slide 22: Conclusion
The documentation is OK.
The abundance data of all species have similar trends as the DFMS number density data.
The ratio tests do not work very well for some species and for a certain period. It can also be caused by some issues in the number density data.
The user may need to be more careful when using CO data and data near the end of the mission.