## Slide 1
New Horizons Solar Wind Around Pluto
SWAP
Reviewed by S. Joy (secondary)
Low Energy Plasma Instrument consisting of a Retarding Potential Analyzer (RPA), and Electrostatic Analyzer (ESA), and a deflector (DFL).
Mass: 3.29 kg
Power: 2.84 W
Energy (min,max): 30-7700 eV
Energy Resolution: 1 eV
Field of View: 270o x 10o
Angular Resolution: N/A
Geometric Factor 1.8x10-3cm2 sr eV/eV
Sweep Time (128 steps) 64 s
Accumulation Time 0.39 s

## Slide 2: NH-SWAP Data Set Evaluation Tools
  Evaluation -
  Machine: Dell XPS 15 9510
  Operating System: Windows 10

## Slide 3
  Datasets: nh-x-swap-2-pluto-v2.0 nh-x-swap-2-kem1-v6.0 nh-x-swap-3-kem1-v6.0
  Volumes:
  NHKESW_1001 NHKESW_2001
  Volume Level Files
  AAREADME – files are acceptable
  VOLDESC – files are acceptable

## Slide 4
  Comments on review procedure
  The catalog, documents, and calib directories of these volumes are nearly identical, and most of their contents have been previously reviewed many times.
  I have taken advantage of this fact to reduce the review effort.
  I used the folder compare option in BeyondCompare 3.3.13 to compare like folders across the four volumes, and then compare files contained in the folders. Most of the time, the only variation in the directory contents or the
  file therein were the file time stamps and the data_set_id’s in the label files.
  Once this information was available to me, I only reviewed unique files
  Lastly, I looked at issues raised in the February 2022 review to make sure that they had been addressed in this release.

## Slide 5
  Catalog Directory:
  catinfo.txt - good, includes suggested correction from last review
nh_kem.cat – ok
nhsc.cat – ok
ref.cat – ok
There are no differences between files that should be identical on the two volumes (nh_kem.cat, nhsc.cat, ref.cat, swap.cat, etc.) – good, correct versions included
  dataset.cat (NH-X-SWAP-2-KEM1-V6.0) and
  dataset.cat (NH-X-SWAP-3-KEM1-V6.0)
  are effectively the same file with only the most minor differences

## Slide 6
  Calib Directory:
  calinfo.txt - good
  background_009_dac.tab (lbl) - good
  background_009_dac_jup.tab (lbl) - good
  esa_rpa_v16_energy_binsf_new.tab (lbl) - good
  esa_rpa_v18_energy_binsf_new.tab (lbl) - good
  esa_rpa_v19_energy_binsf_new2.tab (lbl) – good
  esa_shape.tab (lbl) – good
  fov_mask_2d.tab (lbl) – good
  list_energy.tab (lbl) – good
  rpa_shape.tab (lbl) – good
  Beyond Compare of all files to Feb 2022 release versions shows that the
  only changes are to the DSID version (-V5.0 to –V6.0) in the LBL files.

## Slide 7
  Document Directory:
  docinfo.txt (all) - good
  codmac_level_definitions, lunineetal1995, payload_ssr, swap_ssr PDF files all PDF/A format. All previously reviewed and acceptable swap_cal – good, fixed problem with Fig 7 description from -5- review
  soc_inst_icd.pdf (lbl) (errors in equation 3 from -5- review returned after being fixed in the version for the -5- PEPSSI delta review)
  nh_met2utc.tab file is complete.
  data_summary_plots directory contents are ok, plots are useful
  nh_mission_trajectory.tab (lbl) - good
  quat_axyz_instr_to_j2k.asc (lbl) – good
  seq_swap_kem1.tab (.lbl) - good, updated
  seq_swap_kemcruise1.tab (.lbl) – good, complete
  nh_fov.png (lbl) - good
  Document/data_summary_plots Directory:
  Plots available for all days when calibrated data are available Directory listing is overwhelmed by 1 day files, consider subfolders
  Document/traj Directory trajinfo.txt – good traj_2006_2028_1d.tab (lbl, fmt) – ok, unclear where the reconstructed vs. predict boundary occurs in the file based on the kernels listing.

## Slide 8
  Index Directory:
  indxinfo.txt - good, all 3 datasets
  index.tab (lbl) - good, all 3 datasets
  slimindx.tab (lbl) - good, -2- and -3- datasets
  checksum.tab (lbl) - good, all 3 datasets

## Slide 9
  Data Directories:
nh-a-swap-2nh-a-swap-2-kem1-v4.0-kem1-v4.0
nh-a-swap-2-kem1-v6.0
    Data appear to be complete
    Labels validate
    FITS files open in FV and the contents appear to be valid
nh-a-swap-3-kem1-v6.0
    Data appear to be complete except for some missing high-energy channels
    Labels validate
    FITS files open in FV and the APID contents appear to be valid Summary plots show mostly valid data

## Slide 10
Data Directory Contents
The highest energy channels disappear following the gap around 2021 day 200 and continuing through 2022. These channels were not missing in the Feb 2022 review.
Data appear good and complete, except for the missing channels
2021
2022
Annual
Summary Data Plots
Missing Channels

## Slide 11
Annual Summary Plot for 2021 from February 2022 Review
No missing energy channels

## Slide 12
Data Directory Contents
Plot courtesy of R. Frahm
Data are nearly continuous until the early 2022.
Missing high- energy channels more apparent in this display

## Slide 13: Recommendations
In general, both of these datasets are in good shape. As previously noted, the dataset.cat descriptions are very generic and do not contain any specific discussion of these particular data. Since the other documentation is complete, no liens have been written.
Liens: 1) Put updated soc_inst_icd.pdf file on volume (one found on PEPSSI delta review) 2) Sort out missing energy channel issue in -3- dataset, these data exist, not an instrument configuration change
3) Sort out missing Summary Data (0x585) in the -2- dataset (see Rudy’s presentation)
Certification: Delta review required for both in order to verify data completeness.