## Slide 1
New Horizons Solar Wind Around Pluto
SWAP
Reviewed by S. Joy (secondary)
Low Energy Plasma Instrument consisting of a Retarding Potential Analyzer (RPA), and Electrostatic Analyzer (ESA), and a deflector (DFL).
Mass: 3.29 kg
Power: 2.84 W
Energy (min,max): 30-7700 eV
Energy Resolution: 1 eV
Field of View: 270o x 10o
Angular Resolution: N/A
Geometric Factor 1.8x10-3cm2 sr eV/eV
Sweep Time (128 steps) 64 s
Accumulation Time 0.39 s

## Slide 2: NH-SWAP Data Set Evaluation Tools
  Evaluation -
  Machine: Dell XPS 15 9510
  Operating System: Windows 10

## Slide 3
  Datasets: nh-x-swap-2-pluto-v2.0 nh-x-swap-2-kem2-v1.0 nh-x-swap-3-kem2-v1.0
  Volumes:
  NHKESW_1001 NHKESW_2001
  Volume Level Files
  AAREADME – files are acceptable
  VOLDESC – files are acceptable

## Slide 4
  Comments on review procedure
  The catalog, documents, and calib directories of these volumes are nearly identical, and most of their contents have been previously reviewed many times.
  I have taken advantage of this fact to reduce the review effort.
  I used the folder compare option in BeyondCompare 3.3.13 to compare like folders across the four volumes, and then compare files contained in the folders. Most of the time, the only variation in the directory contents or the
  file therein were the file time stamps and the data_set_id’s in the label files.
  Once this information was available to me, I only reviewed unique files
  Lastly, I looked at issues raised in the October 2022 (KEM1) review to make sure that they had been addressed in this release.

## Slide 5
  Catalog Directory:
  catinfo.txt - ok
nh_kem.cat – ok
Nh_kem2.cat - ok
nhsc.cat – ok
ref.cat – ok
There are no differences between files that should be identical on the two volumes (nh_kem.cat, nh_kem2.cat, nhsc.cat, ref.cat, swap.cat, etc.) – good, correct versions included
  dataset.cat (NH-X-SWAP-2-KEM2-V1.0) and
  dataset.cat (NH-X-SWAP-3-KEM2-V1.0)
  are effectively the same file with only the most minor differences

## Slide 6
  Calib Directory:
  calinfo.txt - good
  background_009_dac.tab (lbl) - good
  background_009_dac_jup.tab (lbl) - good
  esa_rpa_v16_energy_binsf_new.tab (lbl) - good
  esa_rpa_v18_energy_binsf_new.tab (lbl) - good
  esa_rpa_v19_energy_binsf_new2.tab (lbl) – good
  esa_shape.tab (lbl) – good
  fov_mask_2d.tab (lbl) – good
  list_energy.tab (lbl) – good
  rpa_shape.tab (lbl) – good
  Beyond Compare of all files to Feb 2022 release versions shows that the
  only changes are to the DSID version (-V5.0 to –V6.0) in the LBL files.

## Slide 7
  Document Directory:
  docinfo.txt – BC reports that the version on -2- dataset includes UTF-8 characters not found on the -3- dataset version. Several characters appear bold in Notepad and UltraEdit on the -2- version. The same error occurs for -2- : lunineetal1995.lbl, quat_axyz_instr_to_j2k.asc, swap_ssr.lbl codmac_level_definitions, lunineetal1995, payload_ssr, swap_ssr PDF files all PDF/A format. All previously reviewed and acceptable swap_cal – good
  soc_inst_icd.pdf (lbl) (errors in equation 3 fixed again)
  nh_met2utc.tab file is complete.
  data_summary_plots directory contents are ok, plots are useful
  nh_mission_trajectory.tab (lbl) - good
  quat_axyz_instr_to_j2k.asc (lbl) – good
  seq_swap_kem1.tab (.lbl) - good
  seq_swap_kem2.tab (.lbl) – good
  nh_fov.png (lbl) - good
  Document/data_summary_plots Directory:
  Plots available for all days when calibrated data are available Directory listing is overwhelmed by 1 day files, consider subfolders
  Document/traj Directory trajinfo.txt – good traj_2006_2028_1d.tab (lbl, fmt) – ok, unclear where the reconstructed vs. predict boundary occurs in the file based on the kernels listing.

## Slide 8
  Index Directory:
  indxinfo.txt - good, all 3 datasets
  index.tab (lbl) - good, all 3 datasets
  slimindx.tab (lbl) - good, -2- and -3- datasets
  checksum.tab (lbl) - good, all 3 datasets

## Slide 9
  Data Directories:
nh-a-swap-2nh-a-swap-2-kem1-v4.0-kem1-v4.0
nh-a-swap-2-kem2-v1.0
    Data appear to be complete
    Labels validate
    FITS files open in FV and the contents appear to be valid
nh-a-swap-3-kem2-v1.0
    Data appear to be complete
    Labels validate
    FITS files open in FV and the APID contents appear to be valid Summary plots show valid data with large hibernation gaps

## Slide 10
Data Directory Contents
Plot courtesy of R. Frahm
nh-a-swap-2-kem2-v1.0
Data look good

## Slide 11
Data Directory Contents
Plot courtesy of R. Frahm
Annual plot included with archive
nh-a-swap-3-kem2-v1.0
Data look good

## Slide 12: Recommendations
In general, both of these datasets are in good shape. As previously noted, the dataset.cat descriptions are very generic and do not contain any specific discussion of these particular data. Since the other documentation is complete, no liens have been written.
Liens: 1) Copy new versions of the document files that appear to have UTF-8 characters from the -3- volume to the -2- volume. These files should be identical on both volumes. docinfo.txt, lunineetal1995.lbl, quat_axyz_instr_to_j2k.asc, swap_ssr.lbl
Certification: Good to certify both -2- and -3-